| Company Name: Site: |  | COSHH Assessment |
| --- | --- | --- |
| Supplier: | Dupont | COSHH Number | 54 |
|  |  | page 1 |
| Assessment By: | Activity: | Review Date | Assessment Date |
|  | Construction usage including cutting, sanding and drilling. |  |  |
|  | Persons/Groups at Risk |  |  |
|  | Site Operative/User of product |  |  |

NAME OF HAZARDOUS SUBSTANCE USED OR CREATED

Substance: Corian Solid Surface

| FLAMMABLE |  | TOXIC |  | IRRITANT |  | OXIDISING |  | HARMFUL |  | CORROSIVE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |  | YES | NO |
|  | ( |  |  | ( |  |  | ( |  |  | ( |  |  | ( |  |  | ( |
| Insert ( in appropriate boxes |

|  | Insert ( in appropriate boxes and add comment below | YES | NO |
| --- | --- | --- | --- |
| Is Manufacturers Safety Data Sheet available? |  | ( |  |
| Does the Substance have a Workplace Exposure Limit (WEL)? |  | ( |  |
| If the substance has a WEL please state. if un-sure check HSE document – EH40 | Inhalable dust 10 mg/m3 per 8 hour |  |  |
| Can a safer substance be used or can the substance be enclosed or extracted. |  | ( |  |
| Will employees be given information and training? |  | ( |  |
| Will Personal Protective Equipment be provided for employees? |  |
| State the standard of RPE (respirators) | Minimum standard of FFP2. | ( |  |
| State the standard of Goggles or Spectacles | BSEN166 as a nuisance inhibitor | ( |  |
| State the standard of Gloves |  |  | ( |
| State the standard of Overalls |  |  | ( |
| State the standard of Boots |  | ( |  |
| Other Equipment | Attach details if YES |  | ( |
| Will Exposure Monitoring and/or Control Measures be required? | Attach details if YES | ( |  |
| Will Health Surveillance be necessary? | Attach details if YES | ( |  |
| Does this Substance need to be disposed of by a Waste Disposal Contractor? | ( |  |
| Have all necessary First-aid and welfare requirements been provided? |  | ( |  |
| Have Storage requirements for the substance been provided / arranged on site? |  | ( |  |
| FIRST AID, FIRE FIGHTING, STORAGE & HANDLING, DISPOSAL AND ACCIDENTAL RELEASE INSTRUCTIONS ARE PROVIDED ON PAGES 2 & 3 if required | Number of Sheets attached to this Assessment |  |
| FIRST AID INSTRUCTIONS |
| Route of Exposure, or Type of Injury | First Aid Treatment |
| Skin Contact | In case of irritation from dust generated from processing of Corian, wash with water. |
| Eye Contact | If particles enter the eyes during processing, immediately flush eyes with plenty of water. Seek medical attention if irritation persists. |
| Inhalation | Inhalation of Corian dust can only occur during processing. If inhalation of dust causes adverse effects, remove to fresh air. If discomfort persists, seek medical advice. |
| Ingestion | If ingestion occurs seek immediate medical attention. Wash out mouth with clean water where appropriate |
| General Information | Ensure that the stated PPE is worn and all staff are informed of the risks, control measures and precautions required when working with the substance. |

| FIRE FIGHTING MEASURES |
| --- |
| Hazard | Measures |
| Fire | Water spray, Dry chemical, Carbon dioxide (CO2), Foam Avoid generating dust; fine dust dispersed in air in sufficient concentrations, and in the presence of an ignition source is a potential dust explosion hazard. |
| Stability | N/A |
| Decomposition Products | Methyl methacrylate monomer n-Butyl acrylate Butyl acrylate |

| MANUFACTURERS INFORMATION |
| --- |
| Manufacturers Name and Address | Du Pont de Nemours (Belgium) BVBA Ketenislaan 1, Haven 1548 B-9130 Kallo Belgium |
| Manufacturers Health & Safety Data Sheet Reference | N/A |
| 24 Hour Emergency Telephone Number | +44-(0)8456-006.640 |
| Regulatory Information: Warning Label Phrases | N/A non-hazardous |

| STORAGE AND HANDLING |
| --- |
| Hazard | Measures |
| Handling | Do not breathe dust. Do not breathe vapours or fumes that may be evolved during processing. Wash hands before breaks and at the end of workday. Minimize dust generation and accumulation. Routine housekeeping should be instituted to ensure that dusts do not accumulate on surfaces. Dry powders can build static electricity charges when subjected to the friction of transfer and mixing operations. Provide adequate precautions, such as electrical grounding and bonding, or inert atmospheres. |
| Storage | No special storage conditions required. |

| DISPOSAL MEASURES |
| --- |
| Hazard | Measures |
| Disposal of collected dusts from Local Exhaust Ventilation or from vacuums. | This may expose the operative to higher concentrations of the dusts therefore; a minimum standard of FFP2 masks are advised. Dusts must be kept contained during disposal and subsequent storage. Disposal to landfill etc must be by a registered carrier. Can be landfilled or incinerated, when in compliance with local regulations. |

| ACCIDENTAL RELEASE MEASURES |
| --- |
| Hazard | Measures |
|  | Corian does not represent a hazard in sheet form. However dust generated from processing Corian should be contained carefully collected and removed. |

| USAGE/EXPOSURE |
| --- |
| Frequency and Duration of use |  |
| Maximum number of people involved in activity |  |
| Quantities stored/used |  |
| Exposure levels | It is recommended that all dust control equipment such as local exhaust ventilation and material transport systems involved in handling of this product contain explosion relief vents or an explosion suppression system or an oxygen deficient environment. Ensure that dust-handling systems (such as exhaust ducts, dust collectors, vessels, and processing equipment) are designed in a manner to prevent the escape of dust into the work area (i.e., there is no leakage from the equipment). Use only appropriately classified electrical equipment and powered industrial trucks. |

- Ensure that adherence to this COSHH Risk Assessment is adhered to at all times.

- Wash at the end of each work shift and before eating, smoking and using the toilet.

- When machining ensure on-tool extraction is fitted and working and all LEV is fully functional.

N.B.  Airborne dust monitoring has indicated that WEL has not been exceeded.

Low level health surveillance is in place in the form of annual health questionnaires.

| Name: | Signature: | Date: | Name: | Signature: | Date: |
| --- | --- | --- | --- | --- | --- |

# Text boxes

Safe System of Work

Operatives Acknowledgement   Corian