| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of Angle grinder |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Cutting of concrete/ stone/ | Dust and electrical | Operatives carrying out the work, operatives working nearby, other contractors, visitors, public. | H | Dust Extraction to be used at all times. FFP 3 Dust masks to be worn Ensure grinder is in good condition and displays a current PAT test | L |
| Cutting of concrete/ stone/clay pipes/metal | Noise | Operatives carrying out the work, operatives working nearby, other contractors, visitors, public. | H | Ear protection to be worn at all times. | L |
| Cutting of concrete/ stone/clay pipes/metal | Flying particles | Operatives carrying out the work, operatives working nearby, other contractors, visitors, public. | H | Goggles or face shield to BS EN 166 4B minimum, to be worn at all times (NOT safety glasses). | L |
| Cutting of concrete/ stone/clay pipes/metal | Vibration | Operatives carrying out the work, operatives working nearby, other contractors, visitors, public. | H | Grinder not to be used for more than 1 hour 30 minutes in an 8 hour shift. | L |
| Cutting of concrete/ stone/clay pipes/metal | Incorrect fitting of disc/bursting of disc. | Operatives carrying out the work, operatives working nearby, other contractors, visitors, public. | M | 1. Discs to be fitted by abrasive wheel trained competent persons. | L |
| Cutting of metal | Fire/sparks | Operatives carrying out the work, operatives working nearby, other contractors, visitors, public. | M | Area to be kept free from combustible materials. Fire extinguisher to be available nearby. Employee to wear flame resistant overalls Hot works permit to be used if work takes place indoors. | L |
| Specific Site Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK