| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Bricklayers Access/Egress |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Vehicular movement | Vehicles colliding with pedestrians/other vehicles or plant. | Bricklayers, Site-based Personnel, Visitors, | H | Site traffic management plan to be established by Site Manager. Plan to be displayed in Site Cabins. Plan to be reviewed at least weekly or after significant changes in site activity/layout. Dedicated pedestrian routes to be established, with physical barriers installed where possible. Plan to be included in Site Induction. Signage to be in place to warn vehicles/pedestrians of dangers. High visibility clothing to be worn on site at all times. | L |
| Walking around site | Slips, trips and falls | Bricklayers, Site-based Personnel, Visitors, | M | Pedestrian walkways to be established wherever practical by the main contractor. Suitable surface (i.e. stoned-up) to be in place. Foundation excavations to be suitable for bricklayers access (i.e. width and depth) Bricks / Blocks to be mechanically loaded as close as practicable to the bricklayers to reduce slips, trips and manual handling problems. Provision to be made for temporary lighting if required | L |
| Visitor parking | Vehicles colliding with pedestrians/other vehicles or plant. | Bricklayers, Site-based Personnel, Visitors, | M | Pedestrian walkways to be established by the main contractor wherever practical, to segregate workers. Suitable surface (i.e. stoned-up) to be in place. High visibility clothing to be worn. Vehicle operators to communicate wth workers to organise delivery / loading and reduce collision risk. Provision to be made for temporary lighting if required. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK