| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
| Description Of Work: | Brush cutter / Strimmer |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Brush cutter / strimmer | Revolving Blades | Operator, other workers, client’s personnel. | H | Ensure the half guard is in place around the blades Wearing face shield with Grade B impact, which includes eye protection. If blade checking is required ensure Strimmer has stopped and isolated prior to maintenance checks. Take care when stopping strimmer due to the blade turning for a short period after releasing the throttle. Heavy Duty abrasive resistant gloves to be worn. Safety boots with steel toe caps to be worn. Adequate space between workers (15 metres minimum) Maintenance of the tool and replacements parts to be reported to Hellens managers. | L |
|  | Transporting the Strimmer when not operational | Operator and other workers in the vicinity | M | Carry the strimmer with it properly balanced and cover the blades to avoid risk of injury from contact with the blades. | L |
|  | Fuel and Ignition sources | Operator and other workers in the vicinity | H | Fuel is extremely flammable; therefore keep clear of naked flames and ignition sources. Do not spill any fuel and use spill kits to collect any spillages. Do not smoke and always switch off when refuelling. Do not refuel with a hot engine. | L |
|  | Work related upper limb disorders and manual handling | Operator | M | Weight of strimmer 6kg Use handle bars to control and harness to support strimmer. Use smooth actions during operations and adjust harness support for individual comfort. Report any muscle strains or back problems to the manager. Ensure clear area for good footing during operation to aid manual handling and reduce trip risk. | L |
|  | Flying particles | Operator, other workers, client’s personnel. | H | Prior to strimming ensure that the area is clear of solid objects. Ensure face visor is worn and heavy duty gloves Ensure that no personnel are within a 15 metre radius Check area for cars and other equipment that could be damaged by fling particles. | L |
|  | Exhaust Fumes | Operator, other workers, client’s personnel. | H | The strimmer is designed for outdoor use only. Do not take indoors due to risk of fume build up. | L |
|  | Noise. | Operator, other workers, client’s personnel, general public, visitors. | M | Wearing of hearing protection when above 80dB(A) The noise levels for the strimmer are 110dB (A) Therefore hearing protection must be worn at all times by the operator. Consider audiometry / health surveillance testing for regular users who are exposed to above noise levels | L |
|  | Weather. | Operator | M | Wet weather gear to be worn if rain. However, preferred to delay works until poor weather clears. | L |
|  | Unauthorised use. | Operator, other workers, client’s personnel, general public, visitors. | M | Lock away strimmer when not in use. | L |
|  | Vibration | Operator | M | Equipment should be serviced and maintained to reduce vibration Blades will be sharp Worn parts will be reported immediately New blades will be purchased and changed if they become blunt. Reduce the period of exposure. Job rotation (sharing the work and vibration exposure between several people) Stagger work activities (breaks) to ensure that workers undertake non vibration exposure activities following vibration exposure. Assess vibration times with strimmer at 8m/s2 (47 minutes trigger time) Health surveillance programme of health checks to identify early signs and symptoms of hand arm vibration syndrome. Workers will be informed on the importance of maintaining blood circulation, keeping warm. Wet gloves must be removed and the welfare facilities will be warm and dry | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK