NORTHERN COUNTIES

SAFETY GROUP LIMITED

Safety Services and Training to Industry

# CDM 2015 PRE-CONSTRUCTION INFORMATION

When drawing up the pre-construction information, each of the following topics should be considered.  Information should be included where the topic is relevant to the work proposed.  The pre-construction information provides information for those bidding for or planning work, and for the development of the construction phase plan.  The level of detail in the information should be proportionate to the risks involved in the project.

# PER-CONSTRUCTION INFORMATION

1	Description of Project

a)	project description and programme details including;

  - key dates (including planned start and finish of the construction phase), and

  - the minimum time to be allowed between appointment of the principal contractor and instruction to commence work on site;

- details of client, designers and other consultants;

- whether or not the structure will be used as a workplace (in which case, the finished design will need to take account of the relevant requirements of the Workplace (Health, Safety and Welfare) Regulations 1992);

d)	extent and location of existing records and plans.

2	Client’s considerations and management requirements

a)	arrangements for;

(i) 	planning for and managing the construction work, including any health and safety goals for the project,

- communication and liaison between client and others,

- security of the site,

- welfare provision;

    - requirements relating to the health and safety of the client’s employees or customers or those involved in the project such as;

- site hoarding requirements,

- site transport arrangements or vehicle movement restrictions,

- client permit-to-work systems,

- fire precautions,

- emergency procedures and means of escape,

- ‘no-go’ areas or other authorisation requirements for those involved in the project

- any areas the client has designated as confined spaces,

- smoking and parking restrictions.

      - Environmental restrictions and existing on-site risks

- Safety hazards, including:

  - boundaries and access, including temporary access – for example narrow streets, lack of parking, turning or storage space,

  - any restrictions on deliveries or waste collection or storage,

  - adjacent land uses – for example schools, railway lines or busy roads,

  - existing storage of hazardous materials,

  - location of existing services particularly those that are concealed – water, electricity, gas, etc,

  - ground conditions, underground structures or water courses where this might affect the safe use of plant, for example cranes, or the safety of groundworks,

  - information about existing structures – stability, structural form, fragile or hazardous materials, anchorage points for fall arrest systems (particularly where demolition is involved),

  - previous structural modifications, including weakening or strengthening of the structure (particularly where demolition is involved),

  - fire damage, ground shrinkage, movement or poor maintenance which may have adversely affected the structure,

  - any difficulties relating to the plant and equipment in the premises, suck as overhead gantries whose height restricts access,

  - health and safety information contained in earlier design, construction or ‘as-built’ drawings, such as details of pre-stresses or post-tensioned structures;

- health hazards, including:

  - asbestos, including results of surveys (particularly where demolition is involved),

  - existing storage of hazardous materials,

  - contaminated land, including results of surveys,

  - existing structures containing hazardous materials,

  - health risks arising from client’s activities.

      - Significant design and construction hazards

- significant design assumptions and suggested work methods, sequences or other control measures;

- arrangements for co-ordination of ongoing design work and handling design changes;

- information on significant risks identified during design;

- materials requiring particular precautions.

      - The health and safety file

Description of its format and any conditions relating to its content.