NORTHERN COUNTIES SAFETY GROUP LIMITED

Safety Training & Services to the Construction Industry

Only trained and authorised employees to use this machine as per ACOP L114

Safe Use Procedures

These machines are used to cut through and stopped mortices

- Ensure chisel and auger are secure

- Only use if trained and authorised.

- Where appropriate use a push stick

- Ensure that all guards are kept adjusted. They should be as close as possible to the workpiece

- Keep hands away from the cutting area

- Report any machinery defects immediately to your supervisor

- Isolate the machine from the power before fitting and adjusting the chisel

- Use support tables for long workpiece lengths

- Ensure the working area on and around the machine is kept clear at all times

- Use all Personal Protective Equipment (PPE) provided by your employer (e.g. hearing defenders etc)

- Use safe Manual Handling techniques at all times

Machine Maintenance and Cleaning

- Do not remove off-cuts, clean the machine or adjust guards whilst the auger/chisel is in motion.

- Maintain the machine in accordance with the manufacturer’s instructions

# Text boxes

Safe Use of Chisel Morticer