| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Dismantling of single storey outer leaf brickwork |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Dismantling of outer leaf of brickwork to single storey building | Manual Handling. | Site Operatives, machine operators, unauthorised visitors. | H | Avoiding manual handling by machine demolition wherever possible. Training in safe manual handling techniques. Carrying out specific assessments where there are repetitive or complex operations. Provide clear access routes to work areas and equipment such as barrows, barrow runs, trolleys, etc. Respiratory protective equipment, goggles or safety glasses. Liaise with neighbours, arrange to work different hours to client. | L |
|  | Electrocution. | Site Operatives, machine operators, unauthorised visitors. | H | Suitably protected 110v supplies and frequent portable appliance testing. Use non-electronic tools. Isolation of all known services and specialist surveys to find others and have them disconnected or re-routed by others. | L |
|  | Contact moving machinery or vehicles. | Site Operatives, machine operators, unauthorised visitors. | M | All machinery movements to be under the control of a qualified Banksman/slinger. Wearing of high visibility clothing. Minimise reversing movements and follow site traffic arrangements in health and safety plan. Traffic and pedestrian segregation | L |
|  | Weather. | Site Operatives, machine operators, unauthorised visitors. | M | Suspend work during strong winds, poor visibility or icy conditions. | L |
|  | Unauthorised access. | Site Operatives, machine operators, unauthorised visitors. | H | Security fences and gates with appropriate signs and possible need for night security watchmen or CCTV. Inspection of gaps in fencing. Sign in and out procedures | L |
|  | Premature collapse of structure | Site Operatives, machine operators, unauthorised visitors. | H | Supervision and carrying out the work by suitable, experienced and competent persons. Calculations by demolition engineer following detailed site investigation. Planned sequence of operations and details of any temporary support and system for transfer of demolition materials to minimise surcharges to the structure. Careful control of the whereabouts of each person on site. | L |
|  | Slips. Trips and falls. | Site Operatives, machine operators, unauthorised visitors. | H | Provide safe access routes. Good housekeeping and use of designated areas for types of waste and reclaimable material. Good lighting. Clean up as demolition progresses to prevent trips. | L |
|  | Vibration White Finger (VWF) | Site Operatives, machine operators, unauthorised visitors. | H | Provide system for monitoring health of operatives. Use modern well maintained equipment, keep hands warm and avoid smoking. Minimise the use of hand held vibrating tools. Health surveillance for those exposed to above 2.5m/s2 | L |
|  | Asbestos / Lead | Demolition operatives and visitors, general public | H | Prior to commencing any demolition an asbestos register must be produced by the client. The survey must be demolition/refurbishment type and the analyst must sample all walls, ceilings etc that need to be demolished. An assessment of paints must also consider lead contamination | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK