NORTHERN COUNTIES SAFETY GROUP LIMITED

Safety Training & Services to the Construction Industry

Only trained and authorized employees to use this machine as per ACOP 114

Safe Use Procedures

These machines are used to produce square shouldered tenons, stepped shouldered and scribed tenons, dimension/profile panel products.

- Fit and properly secure guards and safety devices before starting the machine (hogging units, main and jumping units, and tenon heads)

- Report any faults with the guards or safety devices to your supervisor immediately

- Position components securely on the feed track

- Do not leave the machine unattended whilst the cutters are in motion or running down

- Always use the braking device to stop the machine/cutters

- Ensure the working area is kept clear at all times

- Use all Personal Protective Equipment (PPE) provided by your employer (e.g. hearing defenders etc)

- Ensure safe Manual Handling techniques at all times

Machine Maintenance and Cleaning

- Do not remove off-cuts, clean the machine or adjust guards whilst the blade is in motion

- Maintain the machine in accordance with your training, and if available the manufacturer’s instructions

- Ensure that all trip switches and safety cords are in working order

# Text boxes

Safe Use of Double End Tenoning Machine