| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use and cleaning of dry mortar silo |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| General use | See below | Operatives/other contractors | M | Only trained and authorised operatives to operate silo. | L |
| Starting/use of silo | Contact with wet/dry mortar | Operatives/other contractors | M | Ensure use of nitrile/PVC gloves Ensure use of goggles to BS EN166 Any mortar on skin to be washed off immediately with soap and water (refer to COSHH assessment on cement) | L |
| Starting/use of silo | Electricity | Operatives/other contractors | M | 230v supply from 32A motor rated MCB with 30mA RCD dedicated to exclusive use of silo. Installed by qualified electrician Visual inspection of cables for damage prior to use | L |
| Starting/use of silo | Entanglement | Operatives/other contractors | M | Ensure only trained and authorised operatives use the silo Ensure all guards are closed and secure prior to starting. | L |
| Cleaning/clearing of blockages | Entanglement/electricity | Operatives/other contractors | H | Before any maintenance or cleaning, isolate power supply by switching off at RCB and disconnecting power lead from control panel. Then check that motor will not start by pressing the start/stop button. If mixing screw is jammed, undo motor and swing away from shaft to release any stored tension in screw, prior to removal. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work,

employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK