| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Cutting openings in external walls of an existing structure. |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Forming external openings. | Manual handling. | Demolition, machine operators, unauthorised visitors. | H | Training in safe manual handling techniques. Removal of large blocks of material by machinery. Provide clear access routes to work areas. Provide rubbish chutes to dispose of waste materials or skips on wheels suitable for moving by forklift. Provide wheelbarrows. | L |
|  | Dust. | Demolition, machine operators, unauthorised visitors. | H | Controlled wetting of the surfaces exposed if no electric shock risk. Respirators to be worn minimum of FFP2. An FFP3 will be required if stihl saw used Safety goggles to be worn Liaise with neighbours, arrange to work different hours to client. Consider alternative methods of cutting which produce less dust such as wet cutting diamond chainsaw. Use dustless equipment, i.e. fitted with extractors. Forced air movement. Debris netting of sheeting on any scaffold (scaffold must be designed for this purpose). | L |
|  | Asbestos. | Demolition, machine operators, unauthorised visitors. | H | Carry out pre-demolition refurbishment survey. Asbestos awareness training and emergency plan. Removal by licensed contractor. Cease work if unknown substance if located. | L |
|  | Fall of material. | Demolition, machine operators, unauthorised visitors. | H | Provide scaffolding and inspected by erectors Establish and police exclusion zones, install scaffold fans and debris netting. Suitability strengthened internal floors, propped if necessary. | L |
|  | Electrocution. | Demolition, machine operators, unauthorised visitors. | H | Suitability protected of supplies and frequent user inspection and portable appliance testing. Use of battery equipment. | L |
|  | Noise. | Demolition, machine operators, unauthorised visitors. | H | Provision and enforced wearing of high quality ear defenders when above 85dB(A) Use low noise and remote cutting or breaking equipment, e.g. diamond chain saws. Use machine mounted tools if feasible. | L |
|  | Contact with services. | Demolition, machine operators, unauthorised visitors. | H | Carry out physical survey to identify locations of all services. Remove prior to work commencing, obtain certificate of isolation or disconnection where appropriate or provide sturdy temporary protection. | L |
|  | Weather. | Demolition, machine operators, unauthorised visitors. | M | Provide designed protective sheeting to external scaffold. Waterproof clothing and wellington boots and gloves. | L |
|  | Unauthorised access. | Demolition, machine operators, unauthorised visitors. | H | Temporary covers and barriers Security fencing. Exclusion signs and information during site induction for all persons entering site. | L |
|  | Slips, trips and falls. | Demolition, machine operators, unauthorised visitors. | H | Provide safe access routes. Good housekeeping. Edge protection where there is a risk of falls at edges or openings. Good lighting. Safety footwear. | L |
|  | Collapse of structure. | Demolition, machine operators, unauthorised visitors. | H | Supervision and carrying out of the work by suitable, experienced and competent people. Calculations by engineer and site inspection. Planned sequence of operations. Drawings and manufacturer’s instructions for any temporary support and system for transfer of demolition materials to minimise surcharges to structure. Inspection before and during use of any support equipment. | L |
|  | Falls from height or through fragile materials. | Demolition, machine operators, unauthorised visitors. | H | Maximise the use of remote cutting techniques. Install and maintain edge protection and working platforms or work from mobile elevated working platforms (MEWPS) or similar. Identify unsafe areas by signs and barriers. Install secure temporary covers over holes in floors. | L |
|  | Vibration White Finger (VWF). | Demolition, machine operators, unauthorised visitors. | M | Provide system for monitoring health of operatives. Use modern well-maintained low vibration equipment, keep hands warm and avoid smoking. Use machine mounted tools if feasible. | L |
|  | Explosion. | Demolition, machine operators, unauthorised visitors. | H | Use of gas cutting gear by trained persons only with flashbacks arrestors and non-return valves with bottles secured against tampering and fall. Where possible remove and store in a well ventilated, secure cage outside of working. | L |
|  | Dermatitis. | Demolition, machine operators, unauthorised visitors. | M | System for monitoring skin condition, wearing gloves or waterproof barrier cream. | L |
| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK