| Site: |  | Contract Number: |  |
| --- | --- | --- | --- |
| Assessed by: | Name: |  | Position: |  | Date: |  |
|  | Signed: |  |  |
| Description Of Work: | Use of forward-tipping dumpers |
| Task / Job Component | Hazard | Persons at risk | Risk Rating L/M/H | Controls / Precautions to Reduce Risk | Residual Risk Rating L/M/H |
| Operation of dumper | Overturning | Plant operators, Civils operatives, other contractors, visitors | H | Safe working load not to be exceeded Operator to have CPCS certification Avoid working on excessive gradients ROPS to be fitted and seatbelts worn at all times | L |
| Operation of dumper | Load dropping off skip | Plant operators, Civils operatives, other contractors, visitors | M | Loads must be levelled off and not overloaded Driver must have clear forward field of vision at all times and must not be obstructed by load. | L |
| Operation of dumper | Collision with pedestrians/other vehicles | Plant operators, Civils operatives, other contractors, visitors | M | Operator to have CPCS certification Operator to have appropriate driving licence to drive on public roads Site/road speed limits to be adhered to at all times.. | L |
|  | Unauthorised use | Plant operators, Civils operatives, other contractors, visitors | M | When not in use, dumper must be parked with handbrake applied and keys removed in site compound or other secure area | L |
| Loading of dumper | Injury to operative by machine bucket or load falling | Plant operators, Civils operatives, other contractors, visitors | M | 1. Operators must dismount and turn off dumper during loading operations and stand well clear of loading area. 2. Wear light eye protection when driving dumper if risk of load causing eye problems (i.e. airborne dust or grit) | L |

| Site-specific Activities | Additional Site–specific Hazards | Persons at risk |  | Additional Controls Required |  |
| --- | --- | --- | --- | --- | --- |
|  | Interaction with public/traffic |  | M | 1. Flashing beacons to be switched on at all times. | L |

# Likelihood

How often could the hazard occur? Consider the task, frequency, duration, method of work, employees involved.

# Severity

# How serious would the hazard’s effects be if

realised? Consider the type of hazard, biological, ergonomic, physical and chemical.

# Risk = Likelihood x Severity

E.g. Likelihood (4) X Severity (3) = 12 HIGH RISK